## Slide 1
Supervisor:
Adviser:
Student:
University:
Presentation Date:
Improving the challenge of imaging resolution and field of view in permeability estimation by integrating multiscale imaging of carbonate rocks and Deep Learning
Wetzel.m et al, 2021
IN THE NAME OF GOD
Iman Nabipour, Jafar Qajar, Maysam Mohammadzadeh
Tehran University
September 2024

## Slide 2
3
Methods
4
Discussion
5
Conclusion
1
Introduction
2
Objectives

## Slide 3
Introduction
Literature
Methods
Discussion
Conclusion
Introduction
Digital rock physics (DRP):
Stands at the forefront of porous media characterization.
Integrates cutting-edge tomographic imaging and advanced numerical simulations.
A complement to core-derived laboratory measurements.
Suggestions
1
A typical DRP process
Wetzel.m et al, 2021
A typical MCT setup
Bultreys et al 2016

## Slide 4
Research Objectives
The main objective
Exploring a novel solution to a critical gap in DRP:
The tradeoff between imaging resolution and field-of-view (FOV)
1. Estimating transport properties and their correlation with pore morphology-topology
2.Develop a workflow integrating DRP and machine learning
3. A multiscale imaging for analyzing fluid flow in complex carbonates.
4. An efficient surrogate for Permeability from the low-resolutions images
2
Introduction
Literature
Methods
Discussion
Conclusion
Suggestions
Yufu.N et al. 2020

## Slide 5
Workflow Development
3
1
Imaging and processing
2
Image Registration
3
Segmentation and REV analysis
5
Model development
6
Model evaluation and validation
Introduction
Literature
Methods
Discussion
Conclusion
Suggestions
4
Dataset Construction

## Slide 6
Multiscale/resolution Imaging
4
Introduction
Literature
Methods
Discussion
Conclusion
Suggestions
3.8 cm
3 µm
2 µm
1 µm
MIP test
XRD test: Dolomite

## Slide 7
5
Introduction
Literature
Methods
Discussion
Conclusion
Suggestions
Align the multi-resolution images to locate the overlap region.
Image Processing: 3D Image Registration, Segmentation
Preprocessing
Step 1
Thresholding
Step 2
Post segmentation refinement
Step 3
Statistical analysis | 
Porosity | 0.11
Eff. porosity | 0.90
Tortuosity | 2.15
Int.Mean.Curv | 2x105
Euler | -1356
EqDiameter(um) | 180
Surf Area (um²) | 1.7x106
Pore volume (um³) | 3.3x106
PSD plot | 

## Slide 8
Dataset Construction
6
Introduction
Literature
Methods
Discussion
Conclusion
Suggestions
Data augmentation by morphological filters
LBM (D3Q19) Velocity Field on HR REVs
Reference Permeability variations
Direct pore scale flow simulation

## Slide 9
Model Development
7
Introduction
Literature
Methods
Discussion
Conclusion
Suggestions
The Designed Convolutional Neural Network (CNN) architecture

## Slide 10
Model Development
8
Introduction
Literature
Methods
Discussion
Conclusion
Suggestions
The multiscale resolution-aware network (MRAN) workflow
Hierarchical learning process across scales

## Slide 11
Results and Discussion
Calibration model: The model performance in the registered zone
9
Introduction
Literature
Methods
Discussion
Conclusion
Suggestions
Dykstra-Parson coefficient, Vĸ [-] | STD | Relative error (%) of Mean | Mean [mD] | Transport property
0.775 | 1.755 | 0 | 2.206 | K-LBM
0.765 | 1.765 | 4.54 | 2.307 | K-pred-HR
0.775 | 1.774 | 3.73 | 2.289 | K-pred-MR
0.779 | 1.772 | 3.04 | 2.274 | K-pred-LR

## Slide 12
Results and Discussion
Calibration model: The model performance in the registered zone
10
Introduction
Literature
Methods
Discussion
Conclusion
Suggestions
Residual analysis
The model respects homoscedasticity
Model residuals should ideally exhibit a random distribution around zero, with no clustering

## Slide 13
Results and Discussion
11
Introduction
Literature
Methods
Discussion
Conclusion
Suggestions
Test Data: Domains with different complexity in a wide variety of samples of the MR and LR images from the non-registered entire carbonate plug
Q-Q plot: LR test data
Test images | STD | Geometric mean [mD] | Relative Error [%] | Total data
MR | 0.725 | 1.754 | 16 | 102
LR | 0.705 | 1.612 | 7 | 102

## Slide 14
Conclusion
Despite the complexities and limited size of the training data, the model achieves (R²≈0.96) across scales.
Residual analysis: homoscedasticity, unbiased nature, capable of handling the carbonate media.
The transfer learning enhances the model's performance and generalization, particularly pre-training on 3D EDTs.
11
Introduction
Literature
Methods
Discussion
Conclusion
Suggestions
To resolve resolution-FOV tradeoff in DRP: Developing a multiscsle resolution aware network (MRAN):

## Slide 15
Thank’s for your attention

## Slide 16
References
12
Introduction
Literature
Methods
References
Conclusion
Suggestions
Discussion
1. Wetzel, M., Pore space alterations and their impact on hydraulic and mechanical rock properties quantified by numerical simulations. 2021, Universität Potsdam.
2. Bultreys, T., W. De Boever, and V. Cnudde, Imaging and image-based fluid transport modeling at the pore scale in geological materials: A practical introduction to the current state-of-the-art. Earth-Science Reviews, 2016. 155: p. 93-128.
3. Niu, Y., et al., An innovative application of generative adversarial networks for physically accurate rock images with an unprecedented field of view. Geophysical Research Letters, 2020. 47(23): p. e2020GL089029.
4. Botha, P., Predicting Permeability and Capillary Pressure in Low-Resolution Micro-CT Images of Heterogeneous Laminated Sandstones. 2017, The Australian National University.
5. Rabbani, A., et al., DeePore: a deep learning workflow for rapid and comprehensive characterization of porous materials. Advances in Water Resources, 2020. 146: p. 103787.
6. Santos, J.E., et al., Computationally efficient multiscale neural networks applied to fluid flow in complex 3D porous media. Transport in porous media, 2021. 140(1): p. 241-272.
7. Tang, P., D. Zhang, and H. Li, Predicting permeability from 3D rock images based on CNN with physical information. Journal of Hydrology, 2022. 606: p. 127473.
8. Santos, J.E., et al., Learning a General Model of Single Phase Flow in Complex 3D Porous Media. arXiv preprint arXiv:2310.14298, 2023.